C++ software automated testing

---
Quality loop

---
Introduction

---
Introduction

---
Introduction

---
Introduction

---
Introduction

---
Introduction

---
Introduction

---
V model
http://www.automotivespice.com/

---
Unit tests

---
Class diagram - unit tests

---
Integration tests

---
Class diagram – integration tests

---
Class diagram – integration tests

---
Unit tests vs. Integration tests

---
Unit tests vs Integration tests

---
Unit tests vs Integration tests

---
Unit tests vs Integration tests

---
Unit tests vs Integration tests
class name	unit tests quantity	integration tests quantity	unit tests code coverage lines/functions/branches[%]	Integration tests code coverage lines/functions/branches[%]
smsPlanner	9	8	100/100/66.7	100/100/66.7
smsSender	4	1	100/100/71.4	78.6/100/50
timeKeeper	2	0	100/100/66.7	94.7/100/50
smsDevice	5	0	100/100/64.3	96/100/60.7

---
System tests

---
Class diagram - system tests

---
Unit tests vs integration tests vs system tsts
- unit tests and integration test can be executed on host / build server and also real target device
- system tests have to be executed on real target device beacuse of hardware dependencies

---
Unit tests workflow
- Module owner is providing module to company responsible for unit testing
- Company responsible for unit testing is verifying if module is buildable and ready for tests
- Company responsible for unit testing is splitting module to separated classes tested in parrallel by separated software engineers
- Company responsible for unit testing is reporting issues (bugs, blockers etc.) to module owner
- Company responsible for unit testing is not changing anything in tested module source code
- Company responsible for unit testing is providing unit tests delivery to module owner
- Module owner is doing delivery review and accepting it or sending it back to for further improvements

---
Integration tests workflow
- Module owner is providing module to company responsible for integration testing
- Module owner is providing module documentation, component communication workflow (top -> down and back)
- Module owner is providing integration tests scenarios (prefered form - sequence diagrams)
- If module owner doesnt provide tests scenarios (sequence diagrams) to company responsible for integration testing for created task, company responsible for integration testing will do this based on provided informations from module owner to verify if there is everything available and understood to start
- Company responsible for integration testing is sending tests scenarios (sequence diagrams) to module owner to be accepted
- Module owner is accepting / improving tests scenarios and providing feedback to company responsible for integration testing
- Company responsible for integration testing is verifying if module is buildable and ready to be tested
- Company responsible for integration testing is splitting whole task into subtasks connected with integration tests implementation so whole team is involved (uml documentation, white box concept, mocks, stubs, capturing logs etc.)
- Company responsible for integration testing is reporting issues (bugs, blockers etc.) to module owner
- Company responsible for integration testing may add integration logs to tested module source code
- Company responsible for integration testing is providing integration tests delvery to module owner
- Module owner is doing delivery review and accepting it or sending it back to for further improvement

---
Example tests scenarios

---
Integration tests vs System tests

---
Software/System qualification tests